## Slide 1
Introducing accessEQ
FOR ENHANCED AUDIO
ON THE MAC

## Slide 2
accessEQ Background
80% of hearing aid demos are returned by dissastified users, why?
Speech intelligibility is not improved

## Slide 3
accessEQ Background
SNR determines speech intelligibility,
generic gain does not improve SNR
The hearing aids DSP is computationally weak compared to the Mac’s processor
Can the Mac processor be used to improve
speech intellibility of Mac audio in real-time?
A: accessEQ

## Slide 4
Downloading & Installing accessEQ
  Download the free accessEQ 2024A release (1.0.0.0) from Github @
    https://github.com/TCupolo/accessEQ/releases/download/1.0.0.0/accessEQ.app.zip
  Unzip accessEQ.app.zip to accessEQ.app
  Move accessEQ.app over to the standard Mac Applications folder
  Double click accessEQ.app to run it

## Slide 5
accessEQ App
accessEQ is like a software hearing aid when run as an app. It uses the Mac’s built-in microphone.
Also, the very 1st time its run, it registers as an AUv3 plugin with macOS.
NOTE: to confirm registration was successfull, run auval -a in the terminal, a complete list of installed plugins is returned.

## Slide 6
Even when accessEQ is not being run as an app, it can still function as a plugin with 3rd party hosting apps. There are 2 types of hosting apps:
  SWAC: System Wide Audio Capture
    Enables accessEQ to process all Mac audio real-time
    The primary use case
  DAW: Digital Audio Workstation
    Enables accessEQ to process recorded audio
    A secondary use case
accessEQ Plugin

## Slide 7
NOTE: Both of these apps must be downloaded from the above sites. Around 2022, as an enhanced security measure, Apple decided to make installing any app downloaded outside the Mac App Store intentionally difficult. As a result, the installation process for both of these apps now requires some manual intervention. This consists of changing security settings (which you will be prompted for) and rebooting the Mac before the installation can complete.
  SoundSource by Rogue Amoeba
    Has been around for over 10 years
    Has worked with accessEQ for 3+ years
      Regular updates for bug fixes/new features
    Free 14 day trial then paid
    https://rogueamoeba.com/soundsource/
  eqMAC by Roman Kisil
    Has been around for about 2 years
    Has worked with accessEQ for 1+ year
    Free Basic version, paid Pro version
    https://eqMAC.app
SWAC Hosting App Options

## Slide 8
  Run SoundSource
  Click Add Effect
  Select Tony Cupolo
  Select accessEQ 2024A
  Enable accessEQ 2024A
Using accessEQ with SoundSource

## Slide 9
  Run eqMAC
  Click Add Effect
  Select Tony Cupolo: accessEQ 2024A
  Enable Tony Cupolo accessEQ 2024A
Using accessEQ with eqMAC

## Slide 10
NOTE: AUv2 plugins were known to occasionally cause DAWs to “hang” and there was no easy way to exit this condition other than to reboot. So, Apple came out with the AUv3 format mostly to improve DAW users experience with plugins. AUv3 plugins (like accessEQ) can now be killed independently of the DAW process. This is simply accomplished by running “Force Quit” (under the Apple icon on the menu bar at the top) on the plugin.
  Audacity by The Audacity Team
    Has worked with accessEQ for 3+ years
    Free
    https://www.audacityteam.org/
  GarageBand by Apple
    Has worked with accessEQ for 3+ years
    Free
    Download from the Mac App Store
DAW Hosting App Options

## Slide 11
accessEQ provides 5 different types of EQ, all for the purpose of enhancing audio, and to specifically improve speech intelligibility.
EFFECTS

## Slide 12
The human hearing spectrum spans from 20hz to 20Khz, which accessEQ divides into 10 octaves, with center frequencies:
Frequency EQ
accessEQ uses 6th order filters to ensure the spectral purity of each octave. The graph to the right shows how they compare to other filter orders, which in turn reveals their practical equivalence to brick wall performance.

## Slide 13
Frequency EQ
As a reference, the graph to the right shows how the so- called “speech banana” and other common sounds span the human hearing spectrum as a function of signal amplitude.

## Slide 14
One of the advantages of using accessEQ is it’s inclusion of new effects related to frequency resolution metrics. They determine the SNR required for speech intelligibility. There are 3 key frequency resolution metrics:
  Frequency Discrimination:
    Determines how far apart in frequency 2 different sinusoids, separated in time, must be to be perceived (as melodies).
  Frequency Selectivity:
    Determines how far apart in frequency 2 different sinusoids, present simultaneously, must be to be perceived (as chords).
  Frequency Tuning:
    Determines how far apart in amplitude 2 different sinusoids, present simultaneously, must be to be perceived (as a properly tuned instrument).
Discrimination EQ

## Slide 15
Fletcher and Munson were the first auditory researchers to investigate how loud the human ear perceives different frequencies at the same amplitude. They published their results as a set of equal loudness contours. Later researchers published a more accurate set of measurments as the ISO 226-2003 standard, shown to the right.
Discrimination EQ

## Slide 16
accessEQ converts these equal loudness contours into an equivalent single filter specification. The filter is partitioned into 3 bands as follows:
Discrimination EQ
Each discrimination filters covers the following frequency band:
  Bass: 20Hz - 750Hz
  Mid: 750Hz - 6000Hz
  Treble: 6000Hz - 20000Hz
Testing has determined discrimination is typically most improved with the following settings:
  Bass: 0.15 - 0.25
  Mid: 0.50 - 0.65
  Treble: 0.20 - 0.50

## Slide 17
Spatial EQ
Sound can also be viewed as a field, something that arrives from various directions. Most commonly, audio is delivered as a stereo signal which consists of a left and a right channel. Simple math allows these to be converted into center and side channels. accessEQ provides independent gain controls for all 4 channels, which are displayed intuitively as follows:
NOTE: The Precedence effect allows some delay to be introduced between the center and side channels. This can be used to add more of a “live” feel to both recorded audio and video soundtracks.

## Slide 18
Older music was recorded with vocals in the center and instruments on the side. This was intended to replicate live performance setups as shown below. However, this tended to “mask” the instrument tracks, which can now be brought back out by applying side gain.
In home theater and vehicle settings, spatial EQ likewise allows for compensating out changes in the spatial signal balance due to distributed speaker placements:
Spatial EQ

## Slide 19
SNR is a function of:
  Signal amplitude
  Noise from frequency components
  Noise from spatial components
  Reduced frequency resolution due to mixing multiple audio sources at different loudness levels
For these reasons, accessEQ provides a single control, shown to the right, that “overrides” all effects settings to simplify improving speech intelligibilty real-time. The user only needs to select the desired speech channel (center or side).
Works great on web calls!
Speech EQ

## Slide 20
accessEQ was built for the purpose of enhancing audio quality at the SAME volume. After all the previous effects are applied, the new “wet” signal volume changes. Therefore, a Master Volume control is provided to allow users to adjust the wet volume back to the dry volume level. In this way, the master volume really should be considered a Loudness EQ effect.
Loudness EQ
NOTE: All the hosting apps provide a master “enable/disable” control for plugins. Toggling it, while adjusting the Master Volume, is a simple way to match the wet & dry volume after all other effects have been set.

## Slide 21
Despite all the audio signal processing accessEQ performs real-time, when run from a SWAC hosting app there is minimal impact on the Mac’s processor loading. The screen capture below shows the Mac’s real-time Acitivity Monitor CPU (Quad-Core) Usage bar graph display. SoundSource is hosting accessEQ which is processing the audio QuickTime is playing.
Mac Processor Loading

## Slide 22
accessEQ Open Source Motivation
  50% for better user support
    As the user base grows, it will quickly become to much for one person (me) to support
    Finding the right effect settings can be challenging
      Particularly for non-technical users
  50% for broader platform deployment
    iOS/Android/Windows
      See the Fork Wishlist for details

## Slide 23
End Users
  I’ll create Youtube videos and share them on my YouTube channel:
    https://www.youtube.com/@RaidioTony
  I’ll create an AI chatbot assistant trained on accessEQ, it could be integrated with an accessEQ host app (see the Fork Wishlist).
Developers
  My LinkedIn account is publicly open to developers to connect with me for technical Q&A:
    https://www.linkedin.com/in/tonycupolo/
  I’ll add technical content to the accessEQ Github Wiki
    https://github.com/TCupolo/accessEQ/wiki
Support Plan

## Slide 24
Branch here means features I plan on implementing in future Github releases. Matlab releases come out bi-annually, most contain new audio features. accessEQ releases will follow the same schedule.
Branch Relase | Feature | Description
2024B | Compression | A tri-band compressor that will raise accessEQ status to a full software hearing aid. Matlab already has support for compresion but the UI is too complicated given accessEQ’s other features. So, this release is pending the release of an enhanced plugin UI feature from Matlab. I have submitted a request for such an improvement to Matlab.
2025A | Selectivity EQ | The second frequency resolution feature that will further improve speech intelligibility.
2025B | Tuning EQ | The third frequency resolution feature that will further improve speech intelligibility.
2026A | Speech Extraction | AI can already extract speech from any background but not yet in real-time.
Branch Roadmap

## Slide 25
Fork here means features I hope others will implement in future Github releases.
Fork | Feature | Description
macOS | Audio Server Driver Based SWAC Host | Apple only allows SWAC hosting apps into the Mac App store if they use this method. (SoundSource and eqMAC do not.) Getting an integrated accessEQ SWAC host/plugin app into the Mac App store would be a big adoption driver, particularly if it’s free. An integrated AI chatbot assistant would be a great addtional feature.
iOS | AudioBus Host / iOS App Extensions | Apple doesn’t offer any SWAC type framework on iOS due to their app sandbox policy. However, Audiobus is a highly adopted 3rd party API that allows apps to voluntarily exchange audio data real-time. This opens the door to the possibility of an Audiobus based integrated accessEQ host/plugin app. However, App Extensions for the core Apple iOS apps would also have to be developed to support sharing their audio data with accessEQ over Audiobus.
Windows | SWAC Host | Converting accessEQ to the PC compatible VST plugin format is trivial. However, I don’t know of any SWAC hosting apps for the PC. Further, the Windows audio engine is well known to suffer from large audio latency.
Fork Wishlist